## Slide 1: RISC-V 64K Base Page
路旭
字节跳动内核工程师

## Slide 2
目录
01
/Background
设计与实现
02
/Design
/Future work
CONTENT
背景
未来计划
03

## Slide 3
背景
Part One
1

## Slide 4: Background
64K base page
63
41
29
28
16
15
0
TTBRx
TTBR select
level2 index
level1 index
data offset
...
...
XX
15
0
physical page number
data offset
VA
PA
16
Application | Performance Improvement (Over 4K)
Redis proxy | 100%
Redis Server | 250%
RDS | 20%
NewSQL DB | 10~20%
Object Storage | 50%
Application Performance on Ampere Altra (64K Base Page)
What is 64K base page (CONFIG_ARM64_64K_PAGES)
Why we need 64K base page
  Benefits of ARM V8 64K base page
ARM V8 64K MMU
64K

## Slide 5: Background
64K base page on RISC-V
RISC-V ISA Mannual only supports 4K base page size
What did we do
  Implement 64K base page based on 4K MMU

## Slide 6
设计与实现
Part Two
2

## Slide 7: Design & Implementation
What did we do？
  Implement 64K base page based on 4K MMU
How？
  All problems in computer science can be solved by another level of indirection, except for the problem of too many levels of indirection
  Luckily, there is an existing abstraction layer in Linux
MM
MMU
Arch
Memory
Regard base page as 64K
Regard base page as 4K
Hardware
Software
Eliminate the base page size gap
64K
4K
4K
...
4K

## Slide 8: Design & Implementation
How to eliminate the base page size gap?
  Keypoint: decouple base page and "page table page"
  Per pte_t maps 16 contiguous 4K pages
#define PAGE_SHIFT 16
#define PT_SHIFT 12
#define PTES_PER_PAGE (1 << (PAGE_SHIFT - PT_SHIFT))
/* Page Table entry */ typedef struct { unsigned long ptes[PTES_PER_PAGE]; } pte_t;
#define pte_val(x) ((x).ptes[0])
static inline pte_t pte_mkyoung(pte_t pte)
{ return __pte(pte_val(pte) | _PAGE_ACCESSED);
}
static inline pte_t pte_mkdirty(pte_t pte)
{ return __pte(pte_val(pte) | _PAGE_DIRTY);
}
static inline pte_t __pte(unsigned long pteval)
{ pte_t pte; unsigned int i; for (i = 0; i < PTES_PER_PAGE; i++) { pte.ptes[i] = pteval; if (__pte_present(pteval)) pteval += 1 << _PAGE_PTFN_SHIFT; } return pte;
}

## Slide 9: Design & Implementation
How to eliminate the base page size gap?
  Keypoint: decouple base page and "page table page"
  Per pte_t maps 16 contiguous 4K pages
38
30
29
21
20
12
11
0
satp
pgd index
pmd index
pte index
data offset
pgd_t
...
pmd_t
...
pte2
...
pte16
...
pte1
SV39 VA
4K
4K
4K
...
4K Base Page
38
30
29
21
20
12
11
0
satp
pgd index
pmd index
pte index
data offset
pgd_t
...
pmd_t
...
pte2
...
pte16
...
pte1
SV39 VA
4K
4K
4K
64K Base Page
...
64K
pte_t

## Slide 10: Design & Implementation
So far it is more like self-entertainment
How to get benefits of large base page?
  Svnapot Extension

## Slide 11: Design & Implementation
Svnapot Extension
  Specially encoded PTE (e.g. 64K NAPOT)
    N bit of PTE is 1
    NAPOT_PPN = PPN & ~0b1111
    PA = (NAPOT_PPN << PAGE_SHIFT) + VA[15:0]
  PTEs of same NAPOT is same (Like ARM Contiguous PTE)
    TLB can store only one entry per NAPOT
38
30
29
21
20
15
11
satp
pgd index
pmd index
pte index
pgd_t
...
pmd_t
...
pte1
...
pte1
...
pte1
SV39 VA
64K
0
12
data offset
64K Page Table Walker
1
PA: 0x80000000
0x8000
0b1000
R/W/X
pte1
N bit
PPN
Napot code
Prot
16

## Slide 12: Design & Implementation
Svnapot Extension
  Specially encoded PTE (e.g. 64K NAPOT)
    N bit of PTE is 1
    NAPOT_PPN = PPN & ~0b1111
    PA = (NAPOT_PPN << PAGE_SHIFT) + VA[15:0]
  PTEs of same NAPOT is same (Like ARM Contiguous PTE)
    TLB can store only one entry per NAPOT
38
12
11
0
tag
data offset
tag
XX
11
0
physical page number
data offset
SV39 VA
PA
12
pfn
tag
pfn
...
tag
pfn
...
16 entries per 64K
38
11
tag
tag
XX
physical page number
SV39 VA
PA
pfn
tag
pfn
...
tag
pfn
...
1 entry per 64K
0
data offset
15
12
16
data offset
0
15
4K Entry TLB
64K Entry TLB

## Slide 13: Design & Implementation
64K base page based on Svnapot
  Apply 64K Svnapot for ptes of every 64K base page
static inline void set_pte(pte_t *ptep, pte_t pteval)
{ unsigned long order; for_each_napot_order(order) { if (napot_cont_shift(order) == PAGE_SHIFT) pteval = pte_mknapot(pteval, order); } } *ptep = pteval;
}

## Slide 14: Design & Implementation
64K base page based on Svnapot
  Apply 64K Svnapot for ptes of every 64K base page
38
30
29
21
20
15
11
satp
pgd index
pmd index
pte index
pgd_t
...
pmd_t
...
pte1
...
pte1
...
pte1
SV39 VA
64K
0
16
12
data offset
Page Table Walker with Svnapot
38
30
29
21
20
12
11
0
satp
pgd index
pmd index
pte index
data offset
pgd_t
...
pmd_t
...
pte2
...
pte16
...
pte1
SV39 VA
4K
4K
4K
4K Page Table Walker
...
64K
16

## Slide 15: Design & Implementation
Summary: Benefits of RISC-V 64K base page
Less TLB misses
38
12
11
0
tag
data offset
tag
XX
11
0
physical page number
data offset
SV39 VA
PA
12
pfn
tag
pfn
...
tag
pfn
...
16 entries per 64K
38
11
tag
tag
XX
physical page number
SV39 VA
PA
pfn
tag
pfn
...
tag
pfn
...
1 entry per 64K
0
data offset
15
12
16
data offset
0
15
4K Entry TLB
64K Entry TLB
Less meta data cost
struct page
struct page
...
struct page
...
mem_map
physcal memory
struct page
...
mem_map
physcal memory
struct page
16 struct pages per 64K
1 struct page per 64K

## Slide 16
未来计划
Part Three
3

## Slide 17: Future work
Now
  One stage memory virtualization is adapted
  Two stage memory virtualization is adapted when hypervisor exists
Next
  To be submited to linux community soon
  Support of IOMMU is on the way
  Decouple page table page and base page
    All platforms with extensions like Svnapot / Contiguous PTE can choose their proper page size

## Slide 18: Q & A
更多技术交流
欢迎关注【字节跳动SYS Tech】知乎账号

## Slide 19: 谢谢！

## Slide 20: Appendix
Svnapot Extension
Svnapot PTE (e.g. 64K NAPOT)
  N bit is 1
  NAPOT_PPN = PPN & ~0b1111
  PA = (NAPOT_PPN << PAGE_SHIFT) + VA[15:0]
NAPOT PTE（N bit is 1）
NAPOT PTE PPN

## Slide 21: Appendix
Page table adaption
Per 4K page table page still occupies one 64K base page
60K memory waste per page table page
38
30
29
21
20
12
11
0
satp
pgd index
pmd index
pte index
data offset
pgd_t
...
pmd_t
...
pte2
...
pte16
...
pte1
SV39 VA
4K
4K
4K
...
38
30
29
21
20
12
11
0
satp
pgd index
pmd index
pte index
data offset
60K Waste
...
...
SV39 VA
64K
60K Waste
60K Waste
...
...
...
...
16
4K
4K
4K
64K
64K
64K
4K Base Page
64K Base Page

## Slide 22: Appendix
Page table adaption
Simulate 64K page table in software way
60K memory waste per mm struct
38
30
29
21
20
12
11
0
satp
pgd index
pmd index
pte index
data offset
60K Waste
...
...
SV39 VA
64K
...
...
...
...
16
38
30
29
21
20
12
11
0
satp
pgd index
pmd index
pte index
data offset
60K Waste
...
...
SV39 VA
64K
60K Waste
60K Waste
...
...
...
16
4K
4K
4K
...
4K
4K
4K
...

## Slide 23: Appendix
Limits of RISC-V 64K base page
Requires interrupt file to be 64K aligned
Otherwise, software needs to ensure security between interrupt files located on same 64K page (e.g. via PMP / SPMP / IOPMP)
group 0
group 1
IMSIC M-file
IMSIC S-file
IMSIC M-file
IMSIC S-file
60K align
hart0 M-file (4KB)
60K align
hart1 M-file (4KB)
...
60K align
hartN M-file (4KB)
60K align
hart0 S-file (4KB)
vhart0 VS-file (4KB)
...
...
60K align
vhartN VS-file (4KB)
60K align
60K align
hart1 S-file (4KB)
vhart0 VS-file (4KB)
...
60K align
vhartN VS-file (4KB)
60K align
60K align
hartN S-file (4KB)
vhart0 VS-file (4KB)
...
60K align
vhartN VS-file (4KB)
60K align